## Slide 1
1
School of Electronics Engineering (SENSE)
Project-I (2026)
GaN Based Synchronous Buck Converter with an Improved Gate Driver
Student Name(s):
Sanjay Kumar 23BEC1447 · Aamir Abdullah 23BPS1197 · Amritha S 23BEC1368
Guide:
Dr. Bindu — SENSE
Programme / School:
B.Tech — SENSE, VIT Chennai
Review & Date:
Review-I · 09.09.2026 (Wednesday)
Guide's Signature with Date
Signature: _____________________
Date: _________________________
Approval is mandatory before every review. After signing, scan this slide and keep the scanned copy as Slide 1 of the presentation.
Notes: [15 s] CORE. Project name and the one-line claim: a segmented GaN gate driver, and a measurement of what per-operating-point adaptation is actually worth.

## Slide 2
2
Review-I — 09.09.2026 (5 Marks, 5%)
Focus: Proposed Solution & 50% Work Completion.
Duration: 10 minutes.
Presentation contents:
  Signed & scanned title slide (Slide 1)
  Problem statement and background
  Literature survey — minimum 8–10 recent references
  Existing solutions and their limitations
  Proposed solution, scope and methodology
  50% work completed, timeline, tools & technologies
Mark split-up: Problem clarity & relevance (2), Literature survey quality (1), Proposed solution feasibility (1), Presentation quality (1).
Notes: [skip] SKIP. Template slide.

## Slide 3
3
Problem Statement & Background
Problem Statement:
When one GaN transistor switches, its fast voltage swing pushes charge into the gate of the other transistor, the one that is supposed to stay off. That gate rises to 1.65 V, and only 1.4 V is needed to turn it on. Both devices conduct at once and the supply shorts through them. (That 1.65 V is our device model’s; how much the result depends on the model is itself a finding, and it has its own slide.)
Background & Significance:
GaN half-bridges sit inside EV inverters and battery chargers. GaN is chosen because it switches fast, and that speed is exactly what causes this fault.
Existing Solutions:
Gate drivers that turn the device on in steps, clamp the off gate down, adjust the gap between the two switching edges, and hold the gate at −2 V [1]–[4]. Reported: 30.5 % less overshoot, 75 % less turn-off loss [5]–[7].
Limitations / Research Gap:
Nobody has measured what the re-tuning is worth. Those gains mix two different things: picking one good setting, and changing the setting while the converter runs. Only the second needs a sensor, a lookup table and a controller.
Notes: [60 s] CORE — the 2-mark slide, the biggest block in the review. Land two things: the failure is real and specific (1.65 V on a 1.40 V threshold), and the gap is that prior work conflates 'better fixed settings' with 'settings that adapt'.

## Slide 4
4
The goal, and whether this serves it
The goal. Build a synchronous buck converter for an energy-storage system out of GaN HEMTs, and make it work at the switching speed GaN is bought for. Everything else in this deck exists to serve that sentence.
1. Why GaN at all
Same converter, same job, only the device swapped. At 500 kHz GaN wastes 5.9 W against silicon's 17.3 W. The lead widens to 78 % at 1 MHz and 90 % at light load, and never turns back.
Raising the frequency to shrink the magnetics is nearly free on GaN and ruinous on silicon.
2. What GaN costs you
The same speed that wins is what breaks it. A 1.4 V threshold and 150 pF of drain-to-gate capacitance mean the device that is supposed to be off gets pushed toward on by its partner switching.
Measured: the off gate reaches 1.65 V against a 1.4 V threshold. That is a shoot-through.
3. What we build about it
A segmented gate driver: 8 pull-up steps, 8 pull-down steps, an adjustable dead time, a Miller clamp and a −2 V off rail, driven by an FPGA, so every one of them is a setting that can be changed and measured.
Result: −0.249 V of margin becomes +2.576 V.
So the test is not whether the converter runs. It runs: 100 V in, 48.6 V out at 4.88 A, 97.7 % efficient, open loop at a fixed duty, which is the deck the switching study is measured on; the regulated version holds 50.0 V at 96.1 %. Any textbook buck converter runs. The test is whether the architecture we put around it answers the questions the published work on these drivers leaves open, because that is the only part of this that is ours.
The next slide is that question, gap by gap, with the evidence for each.

## Slide 5
5
Aim, and how we approached it
Aim:
To find out how much of a gate driver’s benefit needs the driver to re-tune itself while the converter is running, and how much comes from choosing one good setting and leaving it fixed.
Proposed Solution:
A GaN buck converter driven by a segmented gate driver: 8 pull-up steps, 8 pull-down steps, an adjustable dead time, a Miller clamp and a −2 V off rail. Every one of them is a setting we can change and measure.
How we approached it:
1. Build the converter and check it converts. 100 V DC in, 48.6 V DC out at 4.88 A: 236.9 W delivered, 97.7 % efficient.
2. Recreate the fault. At the fastest setting the gate that should be off reaches 1.65 V, against a 1.4 V turn-on threshold.
3. Fix it one change at a time, measuring each change on its own run, not all at once.
4. Ask whether one fixed setting is enough, by running the driver at two operating points and seeing whether the best setting moves.
Scope and tools:
In scope: the converter, the driver, its settings, and the FPGA controller. Out of scope: building hardware. Tools: ngspice for every simulation, LTspice to draw the circuit and re-check, Vivado for the FPGA.
Notes: [30 s] CORE — proposed-solution mark. The 720-point control word and the method: exhaustive search at every corner, so each per-corner optimum is a TRUE optimum and not the best of a shortlist.

## Slide 6
6
What a GaN HEMT is
Fig. 1 — Drawn diagram, not simulation output. Silicon MOSFET against GaN HEMT on the properties that govern switching. Device modelled: EPC2010C class, 200 V, 25 mΩ, Vth = 1.4 V (models/egan.lib).

## Slide 7
7
Why GaN and not silicon — measured, same converter
Fig. 2 — Simulated in ngspice. Same buck converter, same job, only the device swapped. Rₓₛ(on) matched 25.0 mΩ GaN against 24.0 mΩ Si, each at its own rated gate drive, so conduction loss is equal by construction and what is left is switching, gate drive and the body-diode recovery GaN does not have. At 500 kHz GaN wastes 5.9 W against silicon's 17.3 W; the lead widens to 78 % at 1 MHz and 90 % at light load (scripts/si_vs_gan_sweep.py).

## Slide 8
8
Why the GaN HEMT causes the problem we solve
Fig. 3 — Drawn diagram, not simulation output. Three device properties and their consequence in a half-bridge: a 1.4 V threshold, 150 pF from drain to gate, and no body diode.

## Slide 9
9
The base paper we build on
 | Zhang, Yu, Leng, Cui, Deng & Ng (2020) — IEEE ISPSD |  |  | 
 | What it does | A segmented gate driver for E-mode GaN HEMTs: the output stage is split into slices, and drive strength is selected by a pattern rather than set by a resistor. |  | 
 | Same device, same architecture | GaN HEMTs in a bridge, a sliced output stage, strength chosen by a code. That is the structure this project starts from. |  | 
 | How we extend it | Theirs is an ASIC with a fixed pattern set, chosen at design time. We make every field programmable from an FPGA — slices, dead time, Miller clamp, off-bias rail — add the clamp and the −2 V rail, and measure what choosing the pattern per operating point is worth. |  | 
W. J. Zhang, J. Yu, Y. Leng, W. T. Cui, G. Q. Deng and W. T. Ng, “A Segmented Gate Driver for E-mode GaN HEMTs with Simple Driving Strength Pattern Control,” in Proc. IEEE 32nd Int. Symp. Power Semicond. Devices ICs (ISPSD), 2020, pp. 102–105.
Notes: [30 s] CORE — literature mark. Do not read the table. Eight references, three verified to page level; point at [3], layout sets loop inductance, which decides our answer.

## Slide 10
We implemented the base paper, then ours
10
Citing a base paper is not a comparison, so we built theirs too. models/zhangdrv.lib is Zhang et al.'s driver: seven slices brought in as a timed pattern across the switching edge, the pattern picked by one bias resistor, with no gate clamp and no −2 V rail, because those two are ours. It runs inside the same sim/dpt.cir, so only the driver differs.
Base paper, at its best setting
+0.407 V
Their staged pattern on its own already clears the 1.4 V threshold, at the best setting in their own stated range.
Ours, constant code, no clamp
−0.249 V
False turn-on. A constant code is worse than their staged one — their idea is real, and we reproduce it.
Ours, active Miller clamp on
+0.570 V
Only just past the base paper. The clamp on its own is not the story.
Ours, clamp + −2 V off-bias
+2.576 V
6.3× the base paper's best margin. This is the version we ship.
What the comparison shows. The base paper stages its slices over time and picks the pattern with one resistor; we add two things they do not have and make every field programmable. Both clear the threshold — theirs works, and we quote it at its best setting — but ours clears it by 6.3× more, and ours is the one whose settings can then be searched in full. Across their own stated range their margin runs +0.407 V down to −0.278 V, so quoting them anywhere worse would be picking the opponent.
Command: python3 scripts/basepaper_compare.py — four ngspice runs, prints this table.

## Slide 11
11
Head to head with the base paper
5.5× to 12.4×, and the lead widens as the corner gets harder.
Fig. 4 — Simulated in ngspice. scripts/headtohead.py: same deck, same GaN, same parasitics; only the driver is swapped. We hold one fixed control word at all four corners; they are re-optimised at every corner, which is more freedom than their own design has. Their margin falls +0.50 → +0.18 V from the mildest corner to the hottest and ours barely moves, because a clamp does not care how hot the device is. Our switch node also slews about twice as fast, so the margin is not bought with switching speed. One caveat: models/zhangdrv.lib is our implementation of the scheme as they (their netlist is not published), run in our testbench with our parasitics. It is not 5.5–12.4× their measured result, and we do not claim it is.

## Slide 12
12
The closest published drivers
Ref | Author(s) & Year | Title / Source | Aim — what the paper sets out to do | Gap we found → what WE fill
BASE PAPER | Zhang, Yu, Leng, Cui, Deng & Ng (2020) | A Segmented Gate Driver for E-mode GaN HEMTs with Simple Driving Strength Pattern Control Proc. IEEE ISPSD, 2020, pp. 102–105 ieeexplore.ieee.org/document/9170108 | Segmented output stage on E-mode GaN: 7 slices, pattern timing 0.5–5 ns, strength set by one external bias resistor | Base paper. Same device, same architecture: E-mode GaN, segmented output stage, strength set by a pattern. Theirs is an ASIC with a fixed pattern set. We make every field programmable from an FPGA and price what the pattern space buys. We fill: the price of the pattern space: what an exhaustive search buys over their fixed pattern set.
11 | Wang, Tao, Xiao, Luo, He, Zhou, Zhang & Wang (2024) | High-Frequency Three-Level Gate Driver for GaN HEMT Bridge Crosstalk Suppression IEEE Trans. Power Electron., 39(1), 1343–1352 ieeexplore.ieee.org/document/10286072 | Three-level drive; capacitor–diode negative rail with a digitally-clamped zero level, to 5 MHz | Recent, GaN, and on exactly our failure mode. It suppresses crosstalk with added passives; we get the same protection from the Miller clamp already in the cell and measure its price at 0.04 %. We fill: whether the setting has to change with the operating point at all. It does not: 2.6 % of baseline.
12 | Wang, Sun, Yan, Ma & Xu (2024) | An Integrated Suppression Method of Both Gate-Source Voltage Oscillation and Crosstalk for GaN HEMT Gate Driver IEEE Trans. Power Electron., 39(11), 14643–14655 ieeexplore.ieee.org/document/10591431 | One driver addressing gate-source ringing and crosstalk together | Confirms the two effects are coupled, which is why our cost function prices loss and overshoot jointly rather than optimising either alone. We fill: both effects in one cost function, showing the objectives genuinely conflict (Pareto, slide 16).
13 | Cai, Ye, Lv & Chen (2026) | A High-Efficient GaN Driver With Hybrid Adaptive Dead-Time Control and Peak Delay Control for Synchronous Buck Converter IEEE Trans. Power Electron., 41(1), 279–290 ieeexplore.ieee.org/document/11146698 | Hybrid adaptive dead-time plus peak delay control on a GaN synchronous buck | The most recent adaptive dead-time driver we found, and it adapts the one field our leave-one-out test shows carries the whole benefit — and only at light load. We fill: which field is worth scheduling. Only dead time, and only at light load; drive strength is worth 0.00 %.
[10] is the base paper: E-mode GaN, segmented output stage, strength chosen by a pattern. All four are verified against the publisher record.
Notes: [25 s] CORE — literature mark. Closest prior work. [8] adapts dead time, the one field we find worth scheduling — and it does so across a 0.2-2 A range, which is exactly the light-load corner our leave-one-out test shows carries all of that benefit. Independent support, not competition.

## Slide 13
The gap this project fills
13
Every paper on these drivers reports one number: how much better it is than a plain driver.
That number hides two separate effects, and they cost very different hardware.
Effect 1: a better fixed setting
Pick one good setting once, at design time. Costs nothing while running: no sensor, no ADC, no lookup table, no controller.
26.5 %
of baseline
Effect 2: adapting per operating point
Change the setting as load, voltage and temperature move. This is the part that needs the sensing hardware.
2.6 %
of baseline
The gap. Nobody separates them. No paper says how much of the benefit actually needs the re-tuning, because separating the two means running every setting at every operating point — and nobody has done that.
Why it matters. Only Effect 2 pays for the sensor, ADC and lookup table. If it is small, that hardware is mostly buying something a design-time choice already gives you.
What we do. 720 settings × 36 operating points, all of them, in ngspice — then report the two numbers separately instead of adding them together.

## Slide 14
14
The driver's settings, and where 720 comes from
Fig. 5 — Drawn diagram, not simulation output. The six fields of the control word and the values swept over each. 6 × 2 × 3 × 5 × 2 × 2 = 720 settings, × 36 operating points = 25,920 transients.

## Slide 15
15
The input — what an operating point is
Fig. 6 — Drawn diagram, not simulation output. Four of the 36 corners every setting is evaluated at: bus voltage, load current and junction temperature.

## Slide 16
16
The output — what is actually measured
Fig. 7 — Drawn diagram, not simulation output. Converter-level output, and the eight quantities extracted from every transient. Definitions fixed in scripts/gansim.py before the sweeps ran.

## Slide 17
17
Crosstalk margin
Fig. 8 — Drawn diagram, not simulation output. Peak gate–source voltage on the off-state device against the 1.4 V threshold, three configurations. Margin is the threshold minus the peak; negative is a false turn-on.

## Slide 18
18
How it works — one use case, start to finish
Fig. 9 — Drawn diagram, not simulation output. One switching edge, followed through. Top row: the controller's decision. Bottom row: the circuit's response. Only the shaded diamond is decided at run time.

## Slide 19
19
The circuit we simulate
Fig. 10 — Drawn and simulated in LTspice. GaN synchronous buck converter, ltspice/BUCK_converter.asc. “Buck” means step-down: 100 V in, 48.6 V out. The two yellow blocks are the segmented gate drivers, the part this project designs. Around them: the 100 V supply with its power-loop parasitics, the two GaN HEMTs, the output filter and a 10 Ω load.
Notes: [30 s] CORE — use this the moment anyone asks what was actually simulated. Trace the red path with a finger: Q1 switches, the SW node moves, charge couples through C_GD into Q2's gate, and Q2 turns on when it should be off. Then point at the clamp and the off-bias mux — those are the two things that fix it. Do not read the component values out.

## Slide 20
20
What ngspice runs
Fig. 11 — A project file, typeset. Not simulation output. Power stage of sim/buck.cir. ngspice reads the circuit as a netlist, not a schematic; it is the same converter the schematic draws. ngspice 48.56 V, LTspice 48.84 V.

## Slide 21
21
Inside the segmented gate driver
Fig. 12 — Drawn and simulated in LTspice. Contents of models/segdrv.lib, drawn as ltspice/SEGDRV_inside.asc: eight pull-up slices from the +5 V rail to the gate, eight pull-down slices to the off rail, and the Miller clamp on its own 0.5 Ω path. It runs: the gate charges to 5.000 V.

## Slide 22
22
How we run ngspice
Fig. 13 — Drawn diagram, not simulation output. One case end to end: the parameters set into sim/dpt.cir, the command, what the simulator wrote, and the window the measurement is taken over. Full load, 100 V / 10 A, no clamp: +1.6486 V against a 1.4 V threshold.

## Slide 23
23
How the work was run
Fig. 14 — Drawn diagram, not simulation output. Method, in the order carried out. Steps 1–3 on one switching edge; steps 4–6 the study built on it.

## Slide 24
24
Which tool did what
Fig. 15 — Drawn diagram, not simulation output. Division of work between the two circuit simulators. All ≈ 35,000 transients are ngspice; LTspice provides an independent check of the crosstalk result.

## Slide 25
25
Demo — ngspice and LTspice, running
Fig. 16 — Demo recording: the converter in ngspice, the crosstalk fault and its fix, the named cases, the Verilog controller, and LTspice running the schematic. 2 min. Click to play.

## Slide 26
26
What we are building — the converter
Fig. 17 — Simulated in ngspice. GaN synchronous buck converter. (a) output charging from zero and settling; (b) three switching cycles; (c) power in against power out. 100 V DC in, 48.56 V DC out at 4.876 A, 97.70 % efficient.

## Slide 27
27
The cases we ran, one at a time
Fig. 18 — Simulated in ngspice. (a) five settings at 100 V / 10 A, one ngspice run each; (b) dead-time sweep at two operating points. Cheapest dead time: 15 ns at full load, 5 ns at light load.

## Slide 28
28
Circuit simulation — the converter
Fig. 19 — ngspice, on screen. scripts/bucksim.py driving ngspice over sim/buck.cir. 100.0 V and 2.426 A in, 48.56 V and 4.876 A out: 242.47 W drawn, 236.89 W delivered, 97.70 % efficient. Peak switch node 115.4 V on a 100 V bus, 15.4 % overshoot, with bus decoupling. Without it: 168 V.

## Slide 29
29
Crosstalk simulation — the fault, and the fix
Fig. 20 — ngspice, on screen. Two runs of sim/dpt.cir. Fastest drive, no clamp, 0 V rail: gate reaches +1.6486 V against a 1.400 V threshold, false_turn_on = 1. Clamp on with −2 V rail: −1.1757 V, margin +2.5757 V, false_turn_on = 0.

## Slide 30
30
Driver simulation — the segmented driver, case by case
Fig. 21 — ngspice, on screen. scripts/cases.py, 13 runs. Part 1: the fix built one change at a time at 100 V / 10 A. Part 2: dead-time sweep at two operating points: cheapest is 15 ns at full load, 5 ns at light load.

## Slide 31
31
ngspice output — what re-tuning is worth
Fig. 22 — ngspice, on screen. scripts/ceiling.py over results/full_corners.csv. 474 of 720 words feasible at all 36 corners. Ceiling on scheduling 3.5 %; per-corner penalty 1.1 / 2.3 / 12.7 / 3.8 %.

## Slide 32
32
ngspice output — the split
Fig. 23 — ngspice, on screen. scripts/grid_analyse.py over 36 corners. Choosing a fixed word (A) 26.5 %; adapting per operating point (B) 2.6 %; B is 8.9 % of the gain. Across 106 overshoot weights (A) stays 23.4–29.0 %, (B) 1.3–6.4 %.

## Slide 33
33
Icarus Verilog output — the controller
Fig. 24 — Icarus Verilog output. iverilog and vvp over rtl/seg_gate_ctrl.v and its testbench. Eight asserted properties, 591 individual assertions, 0 failures.

## Slide 34
34
Vivado output — synthesis
Fig. 25 — Vivado output. Vivado 2024.1.2 on xc7a35t. 20 LUTs and 20 flip-flops strapped, 33 LUTs fully programmable; 200 MHz register-to-register met with 1.996 ns slack.

## Slide 35
35
Result 1 — crosstalk is real, and what fixes it
Fig. 26 — Simulated in ngspice. Gate–source voltage of the off-state device at low-side turn-on, 100 V / 10 A. No clamp: +1.65 V against a 1.4 V threshold. Clamp and −2 V rail: −1.18 V, margin 2.576 V.
The problem is real, and reproduced
1.65 V
peak on the gate that should be off
The threshold is 1.4 V — so it turns on by mistake
2.58 V
margin with the clamp and the −2 V rail
The fault is removed completely
And safety is nearly free
The lowest-energy setting is already safe at three of the four operating points. At the fourth, safety costs 0.04 % more energy — 3.335 µJ against 3.334 µJ.
The clamp is worth 9.7–12.2 % of the blended cost, with no sensor and no controller.
Notes: [40 s] CORE. The problem reproduced and fixed. Point at the red X below the threshold line. Then: safety costs 0.04 % — nearly free once the clamp is present.

## Slide 36
36
The same result in LTspice, on the drawn circuit
Fig. 27 — Drawn and simulated in LTspice. Switch node and off-state gate–source voltage, read from the LTspice .raw file. LTspice +1.647556 / −1.176857 V; ngspice +1.6486 / −1.1757 V on the same netlist.

## Slide 37
37
Result 2 — the driver setting moves the converter
Fig. 28 — Simulated in ngspice. Power lost and peak switch-node voltage against pull-up slice count, measured on the running converter. Eight runs of sim/buck.cir; minimum loss at four slices.

## Slide 38
38
Result 3 — re-tuning is worth only 3.5 %
Fig. 29 — Simulated in ngspice. Cost of one fixed control word against the true per-corner optimum, four operating points, 2,880 transients. Penalty 1.1 / 2.3 / 12.7 / 3.8 %.
What re-tuning is actually worth
3.5 %
the most that re-tuning can ever gain
against the best single fixed setting, over 36 corners (= 2.6 % of baseline). One fixed setting is nearly as good.
The benefit is not spread out. Over 36 points the fixed word costs 0.01 % to 14.2 %; worst is 200 V / 2 A / 125 °C.
3.5 % on the full 36-corner grid — 720 words at each, 25,911 transients. The four-corner study said 5.2 %.
It all comes from the dead time, and that from one operating point. Freezing the dead time costs 5.45 % across four points. Drop the light-load 50 V / 2 A point and it costs 0.00 %: three points want 5 ns, only that one wants 15 ns. So the adaptive hardware shrinks to one light-load detector choosing between two dead times. Freezing the drive strength costs 0.00 % — and that is what these papers actually adjust.
Steady against the device, not the board. Across 21,600 runs no device parameter moves the answer outside 4.3–7.7 %. Halving the board inductance takes it to 13.5 %, and that is layout, not the transistor [3].
Notes: [25 s] CORE. 3.5 %, on 36 corners. Say plainly this is a NEGATIVE result about the adaptive premise and you are reporting it rather than hiding it. Keep it short — slides 18 and 19 do the real work.

## Slide 39
39
Result 4 — the two halves nobody separates
Segmented gate drivers set drive strength by a pattern fixed at design time [10]. Papers on active gate drivers report one number — the improvement over a conventional driver — and that number adds two separate effects together. Only the second needs a sensor, an ADC and a lookup table. Separating them means running every setting at every operating point.
(A) Pick a better fixed setting
26.5 %
no sensing · no LUT
(B) Change it per operating point
2.6 %
needs all of it
(B′) …but one comparator gets 46 % of (B)
1.2 %
a threshold, not a LUT
Adaptation is 8.9 % of the total gain — 2.6 points of 29.0, over 36 operating points; the other 91.1 % comes from the fixed word and needs no sensing. Full sensing, ADC and lookup table justify 4.7 % of the total gain over a fixed word plus one comparator (load current at 10 A, which takes 47 % of the adaptive gap), or 3.4 % over a fixed word plus two. One threshold cannot do better: ten distinct best words spread over the 36 corners, and bus, load and temperature each disagree internally. The four-corner study named bus voltage at 75 V here; on the full grid the comparator is load current.
Notes: [45 s] CORE — the novelty slide, and the one sentence the panel should leave with: 'a full sense-plus-ADC-plus-lookup-table is left justifying 4.7 % of the gain over a fixed word and ONE comparator.' Build it in three steps. (1) Choosing the fixed word well is worth 26.5 %. (2) Adapting per corner adds only 2.6 % — a eleventh of the total. (3) And 47 % of even THAT is capturable with a single comparator on bus voltage, not a lookup table; two comparators reach 61 %, which is the 3.4 % figure. No published work separates these, because separating them needs the exhaustive search rather than a shortlist. If asked why nobody found this: they report one number.

## Slide 40
40
Result 5 — re-tuning only pays below ~2.5 nH
Fig. 30 — Simulated in ngspice. Ceiling on operating-point scheduling against power-loop inductance. Eight values, 7,200 transients. Scheduling pays only below about 2.5 nH.
Notes: [40 s] CORE — the design chart, and the most USEFUL thing in the deck. Do NOT call it a single crossover: eight points show a BAND. Adaptive control pays from about 2.5 nH down, peaks at 13.5 % at 1.5 nH, then FALLS BACK to 8.1 % at 1.0 nH. Say why, because it is the interesting part: at 1.0 nH only 165 of 720 words are still safe, so the fixed word and the per-corner optima are squeezed into the same narrow region and the gap scheduling exploits shrinks. Below ~2 nH feasibility binds, not optimisation. We checked it is not the clamp-chatter artefact — excluding every chatter point leaves all eight ceilings unchanged to the digit. The literature does not state this trade-off because it never separates the fixed and adaptive halves.

## Slide 41
41
FPGA Controller — verified RTL
Three Verilog modules that produce exactly the 720 settings the SPICE model uses.
Dead time is a live register; drive strength is fixed at power-up, worth 5.45 % against 0.00 %.
Eight checks pass in Icarus Verilog, safe reset included. A deliberately broken version is caught 221 times (sh rtl/mutate.sh).
Built in Vivado 2024.1.2 on an xc7a35t FPGA: 20 LUTs, 20 flip-flops, 0.10 % of the chip. 200 MHz timing is met, with 1.996 ns to spare.
Timing is met where the logic runs. The paths that miss are chip-output paths, where the output pad alone takes 3.49 ns of a 4 ns budget: pad delay, not logic.
Fig. 31 — Icarus Verilog output. Icarus Verilog VCD of seg_gate_ctrl.v. The pull-up banks never overlap; the shaded interval is the dead time.
Notes: [BACKUP] BACKUP — the FPGA. If asked: written AND verified, eight asserted properties, then mutation-tested. Dead time gets a live register and drive strength is strapped, because that is what the study found.

## Slide 42
42
Vivado — simulation and synthesis, on screen
Behavioural simulation. Vivado output. fails[31:0] = 0 — every asserted property holds in Vivado's own simulator, a third tool after Icarus and the mutation test.
Synthesis console. 33 LUTs programmable against 20 strapped — the cost of programmability, printed by the tool.

## Slide 43
43
The architecture, end to end
The gap we found in our own work
The controller was verified in Icarus. The power stage was verified in ngspice. The two never touched.
The FPGA emits eight thermometer-coded wires per bank. The SPICE driver took an integer slice count. A fault in the decoder would have passed the Verilog bench and stayed invisible in every figure ngspice produced.
What we did about it
rtl/seg_gate_ctrl_dpt_tb.v reproduces the double-pulse schedule at the real 200 MHz clock, letting the RTL's own dead-time generator make the edges.
Its VCD becomes sixteen PWL sources, one per wire, into models/segdrv_bus.lib. Same deck, same devices, same measurement — only the slice selection changes.
 | margin, RTL bus | margin, .param | difference
clamp off | −0.242 V | −0.249 V | 0.007 V
clamp on | +0.651 V | +0.570 V | 0.081 V
Worst disagreement anywhere: 0.081 V — and it is timing, not encoding. The ideal stimulus turns the low side on at 2.015 µs; the RTL's dead-time generator puts it at 2.0175 µs. The clamp's sign change, which is this project's central claim, is now produced by the actual logic rather than by a parameter.
And it found a real bug, which is the whole argument for doing it: dead time is (dt_cycles + 1) × 5 ns. The counter loads and then counts down through zero, so 15 ns is 2 cycles, not the obvious 15/5 = 3. Anyone mapping our swept dead-time grid onto hardware by dividing by the clock period builds a driver that is one cycle slow at every operating point, and neither half of the verification could have seen it alone.

## Slide 44
44
Closing the loop
The loop holds 50 V. Open loop walks to 60 V.
Fig. 32 — Simulated in ngspice. sim/buck_closed.cir runs the same power stage and the same segmented drivers, now regulated by a type-III loop and then disturbed on purpose. Closed loop 50.01 / 50.00 / 50.00 V through a 2× load step and a 100 → 120 V line step; worst error 0.01 % against open loop's 20.0 %. Load step recovers in 4 µs, line step in 22 µs. Ripple 0.25 %, efficiency 96.1 %, start-up overshoot 3.8 %.

## Slide 45
45
Does the result depend on the model?
Only the shipped design is safe under every model we tried.
Fig. 33 — Simulated in ngspice. Two assumptions carry every margin in this deck, and each was replaced and re-run. scripts/silicon_check.py rebuilds the output stage in real SKY130 5 V transistors; scripts/capmodel_check.py swaps the junction diodes for a charge capacitance. The ordering survives both. Two things do not: the clamp on its own gives +0.03 V on real devices rather than +0.57, and the no-clamp row changes sign between capacitance laws — so “the constant word causes false turn-on” is model-dependent, and we say so.

## Slide 46
46
Does the architecture close the gaps?
Nine gaps in the published work, what our architecture does about each, and the evidence. Every row names the script that produces it.
Gap in the published work | What the architecture does | Evidence | Status
Segmented drivers report one number. Nobody separates a better fixed setting from live re-tuning. | 720 control words × 36 operating points, every combination run. | Fixed 26.5 %, adaptive 2.6 % — adaptive is 8.9 % of the gain, on 36 corners (novelty.py). | CLOSED
Nobody says how much controller the adaptive part justifies. | A complexity ladder: constant word → one comparator → two → full lookup table. | One comparator (load current at 10 A) takes 47 %. 4.7 % is left to justify a sense + ADC + LUT (controller_ladder.py). | CLOSED
Prior segmented drivers stage the slices but carry no Miller clamp and no negative off rail. | 8 + 8 slices plus a clamp plus a −2 V off-bias, each measurable on its own. | Base paper at its best +0.407 V; ours +2.576 V — 6.3× (basepaper_compare.py). | CLOSED
The driver is asserted to be programmable; the logic is rarely synthesised. | seg_gate_ctrl.v, thermometer-coded, with its own dead-time generator. | 8 properties in Icarus; 20 LUT / 20 FF on xc7a35t, 200 MHz met, 1.996 ns slack. | CLOSED
Controller and power stage are verified separately and never made to meet. | The RTL's own VCD drives the SPICE slices — one source per wire, no integer in between. | Margins agree to 0.081 V, and it found a one-cycle dead-time error (rtl_cosim.py). | CLOSED
Whether a fitted schedule generalises to an unseen operating point is never tested. | Leave-one-corner-out: fit the comparator on three corners, test on the fourth. | Identical to the global fixed word on all 36 held-out corners. Nothing — and we say so. | ANSWERED, NEGATIVE
Segmented-driver papers characterise one switching edge. The converter is never closed-loop regulated. | A type-III loop around the same power stage and the same drivers, then disturbed on purpose. | 0.01 % error through a 2× load step and a 20 % line step; open loop walks to 60 V (closedloop.py). | CLOSED
Segmented output stages are published as ideal switches. Whether the result survives real devices is untested. | The same output stage rebuilt in SKY130 5 V transistors and re-run. | Sign and ordering both survive, but the clamp on its own turns out to give only +0.031 V (silicon_check.py). | CLOSED
All of the above is simulation. | — | No silicon measured. The driver is now rebuilt on a real PDK; the GaN model has no equivalent check. | OPEN → Review-III
Does it serve its purpose? Yes, for a simulation study, and that is what it is titled as. Seven gaps closed, one answered in the negative, which is a result rather than a failure, and one that needs a bench. The honest summary is that the architecture is finished and the measurement of it on real silicon is not.

## Slide 47
47
Work Completed — 90 %
Counted, not asserted. 12 blocks, weighted by how much of the project each is. 10 are finished. The weights are on the slide so they can be argued with.
 | Block of work | Weight | Evidence, or why not yet
✔ | The converter itself, built and converting | 8 | 100 V → 48.6 V at 4.88 A, 97.7 % efficient (buck.cir)
✔ | The device choice justified against silicon | 8 | 5.9 W vs 17.3 W at 500 kHz; 3 sweeps, 4 duty profiles
✔ | The base paper implemented, not just cited | 10 | zhangdrv.lib in our own deck, quoted at their best, +0.407 V
✔ | The segmented driver; the fault reproduced and fixed | 12 | −0.249 V → +2.576 V, one change at a time
✔ | The full study: 720 words × 4 corners | 12 | 60,533 transients over 36 corners; fixed 26.5 % vs adaptive 2.6 %
✔ | How much controller that justifies | 8 | ladder + leave-one-corner-out; two implementations agree
✔ | FPGA: RTL written, verified, synthesised, timing met | 12 | 8 properties; 20 LUT / 20 FF; 200 MHz, 1.996 ns slack
✔ | The two halves made to meet in one simulation | 5 | RTL VCD drives the SPICE slices; agree to 0.081 V
✔ | Closed-loop regulation, disturbed on purpose | 8 | type-III loop: 0.01 % error through a 2x load and a 20 % line step
✔ | Transistor-level output stage, on a real PDK | 7 | SKY130 5 V devices: sign and ordering of the result both survive
— | Place-and-route on a chosen board | 3 | Needs real package pins and an MMCM for the clock
— | A hardware half-bridge, measured | 7 | Review-III. Until then this is a simulation study, and is titled as one
90 of 100 done. Review-I's rubric asks for 50 %. We are past it because this is a simulation study and the simulation half is finished. The remaining 10 % is place-and-route on a chosen board and a hardware half-bridge on a bench, and no amount of further simulating will deliver either.
Stated plainly: the architecture is finished. The measurement of it on real silicon is not.
Notes: [40 s] CORE — the 50 %-completion requirement. Five claims, each with a number. If asked 'is this really 50 %?': the search is complete, stress-tested, and both objections to it - layout and EMI - have been tested rather than argued. What remains is silicon and hardware.

## Slide 48
48
Where we are, and what is next
Where we are
90 % by the count on the previous slide. The converter is built and regulating, the fault is reproduced and fixed, the 720-word study is run, the controller is written, verified and synthesised, its output drives the SPICE power stage directly, and the driver has been rebuilt in real transistors.
What is actually left — and it is not more simulating
Place-and-route on a chosen board. Synthesis is done; the flow stops there because the XDC pins are placeholders. Doing it properly also means driving the 200 MHz clock from an MMCM rather than straight off a pin, which is what makes 34 clock-to-pin paths fail today.
A hardware half-bridge, measured. This is the whole of the remaining honest risk. Everything in this deck is a simulation of a converter that has never been built, and one behavioural GaN model underlies all of it.
Also worth doing: transcribe the silicon MOSFET datasheet digits rather than using datasheet-class values, and re-run the ceiling on the transistor-level stage now that it is known to work.
Notes: [30 s] CORE — the timeline and tools requirement. M1-M6. If asked what could go wrong: M1, the PDK — a 1.8 V / 3.3 V teaching PDK cannot take a 5 V rail.

## Slide 49
49
Conclusion & next steps
What the data supports
The converter works: 100 V DC in, 48.6 V DC out at 4.88 A — 236.9 W, 97.7 % efficient.
Picking the setting well: 26.5 %. Changing it per operating point: 2.6 %.
One comparator — load current at 10 A — gets 47 % of that 2.6 %; two comparators get 61 %.
What to build: one fixed setting plus one bus-voltage comparator — not a sensor, an ADC and a lookup table.
The FPGA half is real: 20 LUTs and 20 flip-flops, 200 MHz met with 1.996 ns to spare.
What is next
Review-II — close the loop on the converter, then re-run the setting study with it closed.
Review-III — measure what a two-setting controller saves at the light-load point, where the best dead time differs.
Every number in this deck is regenerated by a named script, in ngspice or in Vivado — 60,533 transient simulations across every study.
Notes: [35 s] CORE. Close on what the data supports and what it now answers. Do NOT concede EMI as a limitation any more - it was tested: pricing it makes scheduling worth LESS, 5.95 % down to 0.15 %. State the remaining limits yourself instead: the two EMI measures disagree about drive strength, and no silicon has been measured. Do NOT concede the single device model any more either - 24 devices were sampled with Vth, gm, Cgs and Cgd varied jointly, the shipped word stays safe on every one, and the ordering survives on every one.

## Slide 50
50
References (1–15)
[1] Z. Zhang, F. Wang, L. M. Tolbert and B. J. Blalock, “Active Gate Driver for Crosstalk Suppression of SiC Devices in a Phase-Leg Configuration,” IEEE Trans. Power Electron., vol. 29, no. 4, pp. 1986–1997, Apr. 2014.
[2] R. Xie, H. Wang, G. Tang, X. Yang and K. J. Chen, “An Analytical Model for False Turn-On Evaluation of High-Voltage Enhancement-Mode GaN Transistor in Bridge-Leg Configuration,” IEEE Trans. Power Electron., vol. 32, no. 8, pp. 6416–6433, Aug. 2017.
[3] D. Reusch and J. Strydom, “Understanding the Effect of PCB Layout on Circuit Performance in a High-Frequency Gallium-Nitride-Based Point of Load Converter,” IEEE Trans. Power Electron., vol. 29, no. 4, pp. 2008–2015, Apr. 2014.
[4] B. Li, G. Zhang, C. Li, G. Wang, S. Liu and D. Xu, “Crosstalk Suppression Method for GaN-Based Bridge Configuration Using Negative Voltage Self-Recovery Gate Drive,” IEEE Trans. Power Electron., vol. 37, no. 4, pp. 4406–4418, 2022.
[5] X. Chen, H. Peng, S. Song, Q. Tong and Y. Kang, “A Novel Control Strategy for Optimal Tradeoff between Overshoot and Switching Loss Based on Double Closed-Loop Self-Regulating Active Gate Driver,” IEEE Trans. Power Electron., vol. 39, no. 10, pp. 13033–13043, 2024.
[6] W. Song, T. Hu, J. Chen, T. Tang, H. Yue and G. Liu, “A Self-Regulating Active Gate Driver of Voltage Overshoot Suppression for SiC MOSFETs Under Variable Load Current Conditions,” IEEE Trans. Power Electron., vol. 40, no. 8, pp. 10623–10634, 2025.
[7] C.W. Kuo, T.W. Wang, L.C. Chen, C.C. Tu, Y.K. Hsiao and P.H. Chen, “Universal Active Gate Driver IC With Closed-Loop Timing Control and Gate-Sensing Technique for Silicon Carbide Power Devices,” IEEE Trans. Power Electron., vol. 40, no. 4, pp. 5120–5129, 2025.
[8] G.H. Thuc and C.J. Chen, “An Integrated Driver With Dual-Edge Adaptive Dead-Time Control for GaN-Based Synchronous Buck Converter,” IEEE Trans. Ind. Appl., vol. 60, no. 6, pp. 9157–9170, 2024.
[9] H. Takayama, T. Okuda and T. Hikihara, “Digital Active Gate Drive of SiC MOSFETs for Controlling Switching Behavior — Preparation Toward Universal Digitization of Power Switching,” Int. J. Circuit Theory Appl., vol. 50, no. 1, pp. 183–196, 2022.
[10] BASE PAPER — W.J. Zhang, J. Yu, Y. Leng, W.T. Cui, G.Q. Deng and W.T. Ng, “A Segmented Gate Driver for E-mode GaN HEMTs with Simple Driving Strength Pattern Control,” in Proc. IEEE 32nd Int. Symp. Power Semicond. Devices ICs (ISPSD), 2020, pp. 102–105.
[11] X. Wang, M. Tao, J. Xiao, D. Luo, M. He, Q. Zhou, X. Zhang and M. Wang, “High-Frequency Three-Level Gate Driver for GaN HEMT Bridge Crosstalk Suppression,” IEEE Trans. Power Electron., vol. 39, no. 1, pp. 1343–1352, 2024.
[12] L. Wang, X. Sun, Y. Yan, M. Ma and D. Xu, “An Integrated Suppression Method of Both Gate-Source Voltage Oscillation and Crosstalk for GaN HEMT Gate Driver,” IEEE Trans. Power Electron., vol. 39, no. 11, pp. 14643–14655, 2024.
[13] Y. Cai, D. Ye, W. Lv and Z. Chen, “A High-Efficient GaN Driver With Hybrid Adaptive Dead-Time Control and Peak Delay Control for Synchronous Buck Converter,” IEEE Trans. Power Electron., vol. 41, no. 1, pp. 279–290, 2026.
[14] Y. Zheng, S. Zhao, P. Agarwal, F. Liu, Y. Zhao and A. Mantooth, “A Multi-Level Turn-Off Gate Driver for Crosstalk Noise Suppression of GaN HEMTs,” IEEE Open J. Power Electron., pp. 1–15, 2026.
[15] M.K. Banda, S. Madichetty, D.M. Natham and S. Koduru, “An Event-Triggered Dual-Polarity Gate Clamp for GaN HEMT Gate Oscillation Suppression,” IEEE Trans. Power Electron., vol. 41, no. 9, pp. 14402–14405, 2026.
Notes: [skip] Reference list. Leave up during questions.

## Slide 51
51
References (16–30)
[16] Z. Yuan, H. Li, M. Zhang, Z. Yang, S. Zhao, H. Wang, X. Wang and L. Ding, “Influence of Negative Gate Bias on Crosstalk Spike in SiC MOSFETs Half-Bridge Circuit,” IEEE J. Emerg. Sel. Topics Power Electron., vol. 14, no. 3, pp. 3217–3229, 2026.
[17] L. Zhang, K. Wang, S. Guo and B. Zhu, “A Gate Driver for Crosstalk Suppression of eGaN HEMT Power Devices,” J. Low Power Electron. Appl., vol. 15, no. 3, pp. 38, 2025.
[18] J. Wu, “Parallel arrangement of MOSFETs, effective suppression of crosstalk: A new gate driver topology,” iEnergy, vol. 2, no. 3, pp. 163–163, 2023.
[19] Y. Mikhaylov, G. Buticchi and M. Galea, “A gate driver for parallel connected MOSFETs with crosstalk suppression,” iEnergy, vol. 2, no. 3, pp. 240–250, 2023.
[20] W. Liu and H. Min, “A Load Adaptive Active Gate Driver with Fast-Switching Three-Level Current Source for Overshoot Suppression in GaN-Based Half-Bridge Converters,” IEEE Trans. Power Electron., pp. 1–8, 2026.
[21] R. Chen, F. Wang, H. Bai and L.M. Tolbert, “A Simple Gate Driver Circuit for Turn-on Overvoltage Suppression of 10 kV SiC MOSFETs With Temporarily Lowering Gate Voltage During dv/dt,” IEEE Trans. Ind. Electron., pp. 1–6, 2026.
[22] D. Yu, M. Yang, L. Yin, K. Hu, W. Zhang and Q. Fu, “A Dual-Loop Active Gate Driver With Independent Voltage Slew Rate and Overshoot Control for Switching Loss Optimization of SiC MOSFETs,” IEEE Trans. Ind. Electron., pp. 1–12, 2026.
[23] P. Xiang, R. Hao, J. Cai and X. You, “An Active Gate Driver of SiC MOSFET Module Based on PCB Rogowski Coil for Optimizing Tradeoff Between Overshoot and Switching Loss,” IEEE Trans. Power Electron., vol. 38, no. 1, pp. 245–260, 2023.
[24] S. Fukunaga, H. Takayama and T. Hikihara, “Slew rate control of switching transient for SiC MOSFET in boost converter using digital active gate driver,” IET Power Electron., vol. 16, no. 3, pp. 472–482, 2022.
[25] C. Xu, P. Fu, X. Liao, Z. Zhu and L. Liu, “An Integrated Driver With Real-Time Predictive Dead-Time Optimization Technique for GaN-Based Synchronous Buck Converter,” IEEE J. Emerg. Sel. Topics Power Electron., vol. 13, no. 3, pp. 3173–3183, 2025.
[26] C. Chen, P. Chiu, Y. Chen, P. Wang and Y. Chang, “An Integrated Driver With Adaptive Dead-Time Control for GaN-Based Synchronous Buck Converter,” IEEE Trans. Circuits Syst. II, vol. 69, no. 2, pp. 539–543, 2022.
[27] J. Tan, Z. Zhou and G. Zou, “A Programmable Gate Driver Module-Based Multistage Voltage Regulation SiC MOSFET Switching Strategy,” Electronics, vol. 13, no. 22, pp. 4379, 2024.
[28] C. Chen, P. Wang, S. Li, Y. Chen and Y. Chang, “An Integrated Driver With Bang-Bang Dead-Time Control and Charge Sharing Bootstrap Circuit for GaN Synchronous Buck Converter,” IEEE Trans. Power Electron., vol. 37, no. 8, pp. 9503–9514, 2022.
[29] G.H. Thuc, M. Tsai, C. Chen, J. Fu, W. Wu and W. Lin, “A Current Source Gate Driver with Dual-Edge Adaptive Slew Rate for GaN Devices,” in Proc. 2026 IEEE Applied Power Electronics Conference and Exposition (APEC), 2026.
[30] G. Wu, Y. Huang, Y. Chen and C. Chen, “Closed-loop Slew Rate Control of Active Current Source Gate Driver with Digital Implementation for SiC MOSFET,” in Proc. 2025 IEEE Energy Conversion Conference Congress and Exposition (ECCE), 2025.
All 30 verified against the publisher record — authors, volume, issue and pages resolved through Crossref by DOI and title, not transcribed by hand.

## Slide 52
52
Thank you
GaN Based Synchronous Buck Converter with an Improved Gate Driver
Amritha S 23BEC1368 · Sanjay Kumar 23BEC1447 · Aamir Abdullah 23BPS1197
Guide: Dr. Bindu — SENSE, VIT Chennai
Everything in this deck runs on request: github.com/Amritha902/gan-driver